Component Framework Concepts
Controller
Keymaster
RT Services
(optional)
Configuration,
Control & Status
App. Component
Configuration,
Control & Status
App. Component
Configuration,
Control & Status
RT-callback
Data
Source
Data
Source
Data
Sink
Data
Source
Data
Sink
Other data sinks
App. Component
RT service
Request

---
Component Framework Concepts
Components Contain the following Interfaces:
Control/Configuration { init, run, stop, reinit, ... }
Status/Error Reporting [combine with control?]
Data Exchange
Component specific interfaces (optional and application defined)

---
The Controller
- Controller is application defined, but should follow standardized control sequence
- Default implementation in framework
- Additional control states may be defined as long as the standard states/event are left intact
- Controller is instantiated by main program

---
‘The Keymaster’
- Keymaster stores both ‘static’ configuration file data as well as runtime information.
- Implemented as key-value store. Keymaster is unaware of the information it stores.
- Keymaster presents well defined interface to Controllers and Components using 0MQ
  - Keymaster clients easily written for any language that supports 0MQ (Python & C++ clients provided)
- Keymaster publishes changes to all subscribers
- Components report status and state changes to Keymaster (and in turn to Controller)

---
Keymaster (cont.)
- Data representation in YAML (YAML Ain’t Markup Language)*
  - human readable
  - data serialization standard
  - well supported by multiple libraries
- static configuration
  - config file
- dynamic state; YAML nodes kept in Keymaster memory
* yaml.org

---
Keymaster configuration
Application components
Connections
(operating modes)

---
‘Generic Component’
Well defined Keymaster and
Configuration Interface
Optional Real-time
 services
interface
Control/Status/
Keymaster I/F
RT Entry pts
Well defined basic states allows
Component reuse even if
Application Controllers differ
Base State
Machine
Application
Specific
Code
D
A
T
A
D
A
T
A
Generalized connection configuration
Supports both 0MQ and RT transports

---
Data Source/Sinks
Configuration file lists available data sinks
Routing lists enumerate the source to sink connections and protocol
Components must agree on binary data format
Implementation of data transport is specified by 0MQ style urls,
Transports include:
0MQ tcp
0MQ udp
0MQ ipc
0MQ inproc
And (non-0MQ) ‘rtinproc’
Sources may bind to multiple transports.
Publish/Subscribe semantics
Interface via a strategy pattern, hiding the details of the transport layer.

---
Component Sequence
Process created, Controller created
Controller creates Keymaster
Keymaster loads configuration file
Keymaster creates the components listed
Components subscribe to Keymaster Pub/Sub and Req/Reply Interfaces
Components bind sources with protocols listed.
Components report ‘Standby’ state to Keymaster.
Controller waits for all components to enter ‘Standby’ state.
Controller posts ‘Initialize’ event to Keymaster (and in turn to Components)
Components initiate connection of sinks to sources listed by Keymaster
Components report ‘Ready’ state to Keymaster
Controller posts ‘Run’ to Keymaster (and in turn Components)
Components enter ‘Running’ state (and report to Keymaster)
Components process data

---
Component Sequence cont.
Controller posts ‘Stop’ to Keymaster (and in turn Components)
Controller waits until all Components enter the ‘Ready’ state
Controller posts ‘Prepare’ to Keymaster
Components enter ‘Ready’ state and report state to Keymaster
Controller posts ‘Run’ to Keymaster
Components enter Running state and report state to Keymaster

---
Component States
Standby
Initial state
Connections made to Keymaster
Sources are bound to Publishers
Sinks unconnected
‘Initialize’ event stimulates transition Ready state
Ready
Components connected, fully initialized and ready to run
Running
Data flows, Components process their data

---
Component Control Events
Initialize
Components should connect Sinks to Sources
Once complete they should enter the Ready state
Stand_down
Only Issued from the Ready state
Should reverse the effect of ‘initialize’ by disconnecting sinks from sources.
Start
Begin processing data
Stop
Component should stop processing data

---
Component States
Running
standby
Ready
‘initialize’
‘stop’
‘stand_down’
(created)
‘start’

---
Optional Real-time Scheduler Service
Where real-time requirements are required, periodic RT-scheduling is available
Currently implementing RT via Xenomai, however, Prempt-RT Linux (RT patches to normal linux kernel) is also supported via Posix.
Setup Sequence:
Component sends callback registration request with scheduling attributes
RT-Scheduler creates the RT thread.
If only an RT-thread is required, the callback need not return
If periodic calling is desired, the callback will be run at the periodic rate, and must return when complete.
RT-scheduler is hard-linked for RT applications – does not use keymaster for communications
RT data interchange must use the rtinproc transport, using other transports will disable real-time context and switch to soft-rt context.

---
Optional Real-time Transport
Real-time transport is setup in non-rt context using 0MQ inproc protocol
Component sinks provide a buffer (ring buffer?) to the source publisher
Publishing is performed in the context of the Component’s RT thread
Publish call will block until buffers have been copied
Unread buffers will be over-written (unlike 0MQ semantics)
Soft-RT to Hard-RT supported using rtinproc transport

---
Hypothetical HPC program
LBW spectral-line
HBW spectral-line
INCO Pulsar
LBW self-test
CODD Pulsar
Keymaster
Architect
nettask
test data
generator
LBW Spectral
line (GPU)
cpu
accumulator
spectral line
FITS writer
PSR
FITS writer
CODD
pulsar processor
(GPU)
INCO
pulsar processor
(GPU)